(Note to Specifier:  This specification has additional instructions included as Hidden Text.  To view this information, Select Tools, Options, and check Hidden Text in the Formatting Marks section of the View Tab.)

# 2004 MASTER FORMAT™ SECTION 10 22 23

Schedules for Wall Features, Partitions, Screens, Panels

3form Edge Felt

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification sections, apply to this Section.

summary

This Section includes the Partition as shown and specified in the described system(s):

Adjust list below to suit Project

Window Shade

Screens

Wall feature

Privacy Curtain

Divider

Related Sections include the following:

Adjust list below to suit Project

Section 10 20 00 Specialty Interior; 10 22 23 Portable Partitions, Screens, Panels

Section 09 54 00 Specialty Ceiling; 09 54 33 Decorative Panel Ceilings

Section 12 24 00 Window Shades

submittals

General:  Submit the following in accordance with conditions of contact and Division 1 specification section 01 33 00 “Submittal Procedures”.

Product Data:  Submit manufacturer’s product data; include product description, fabrication information, and compliance with specified performance requirements.

Shop Drawings:  Include plans, elevations, sections, panel dimensions, details, and attachments to other work.

Samples for Initial Selection:

Submit minimum 2-inch by 2-inch samples.  Indicate full color, pattern variation.

Delete below if mockups are not required

.

Maintenance Data:  Submit manufacturer’s care and maintenance data, including care, repair and cleaning instructions.  Include in Project closeout documents.

quality assurance

Manufacturers Qualifications

Materials and systems shall be manufactured by a company continuously and regularly employed in the manufacture of specified materials for a period of at least five (5) consecutive years and which can show evidence of those materials being satisfactorily used on at least five (5) projects of similar size, scope and location.  At least three (3) of the projects shall have been successful for use three (3) years or longer.

Manufacturer must offer a documented reclaim process that will take back, at the manufacturers cost, panels that are at their end-of life cycle.  Return process is preceded by following requirements highlighted in Section 02 42 00 Removal and Salvage of Construction Materials.

Deliver partitions, systems and specified items in manufacturer’s standard protective packaging.

Do not deliver Wall Feature/Partitions, system, components and accessories to Project site until areas are ready for installation.

Handle materials to prevent damage to finished surfaces.  Provide protective coverings to prevent damage or staining following installation for duration of project.

Project Conditions

Environmental Limitations:  Do not install Partitions until spaces are enclosed and weatherproof, and ambient temperatures and humidity conditions are maintained at the levels indicated for Project when occupied for its intended use.

Warranty

Manufacturer’s Special Warranty on Wall Feature/Partitions:  Manufacturer’s standard form agreeing to repair or replace units that fail in material or workmanship within the specified warranty period.

Warranty Period:  1 year from ship date

The warranty shall not deprive the owner of other rights or remedies the Owner may have under other provisions of the Contract Documents, and is in addition to and runs concurrent with other warranties made by the Contractor under the requirements of the Contract Documents.

PRODUCTS

Manufacturer

Manufacturer:  3form, Inc., Salt Lake City, Utah, USA / telephone 801-649-2500

Materials

3form Edge (Felt)

Non-woven PET Felt

Sheet Size: 8’ Tall, 42” Wide

Basis of Design Product:  The design of Wall Features and Partitions is based on Edge as provided by 3form, Inc.  Products from other manufacturers must be approved by the Architect or Designer prior to bidding in accordance with the Instructions to Bidders and Section 10 60 00 “Product Requirements”.

Sheet minimum performance attributes for Edge:

Flame spread and Smoke developed testing (ASTM E 84).  Material must be able to meet a level of Class A (Flame spread less than 25 and smoke less than 450)

Miscellaneous Materials

General: Provide products of material, size, and shape required for application indicated, and with a proven record of compatibility with surfaces contacted in installation.

Cleaner:  Type recommended by manufacturer.

EXECUTION

examination

Examine substrates, areas, and conditions where installation of Partitions will occur, with Installer present, for compliance with manufacturer’s requirements.  Verify that substrates and conditions are satisfactory for installation and comply with requirements specified.

installation

General:  Comply with manufacturer’s written instructions for the installation of Partitions. Sizes, profiles and other characteristics are indicated on the drawings, additional installation details can be found on the 3form Partner Preliminary Project Review, if applicable.

Installation should be performed by an authorized 3form Partner, if available.

Utilize fasteners, adhesives and bonding agents recommended by manufacturer for type of installation indicated.  Material that is ripped,  hazed or discolored as a result of installation or fabrication methods will be rejected.

Install components plumb, level and rigid, scribed to adjacent finishes, in accordance with approved shop drawings and product data.

We recommend that installation is completed by a 3form Certified Installer. Contact 3form for more information or to get a quote.

cleaning and protection

Protect surfaces from damage until date of substantial completion.  Repair work or replace damaged work, which cannot be repaired to Architect’s satisfaction.

# End of Section 10 22 23

Solid Polymer Fabrication #1 (SPF-1)

# Product:	[Edge]

Color:	[Color name]

Configuration:	[Uniform][Contour][Fan][Stepped][Angle][Arc]

[Diagonal][Jagged][Hourglass]

UV Protection is desirable for applications that will receive direct sunlight.

# Orientation: 	[Partition][Wall][Ceiling]

Repeat Product Data Sheets as required to identify all Varia™ applications.